ITFF/ITTS Access Task Force

How to prepare your carrier for

different accounting rates

for

IFS/UIFN/HCD access from

mobile phones and payphones

Task Force Members

Eugenie D'Aoust, AT&T

Avigal Maor, Bezeq International

Heike Schackmann, Deutsche Telekom

Bill Bolinger, Sprint

Michael Lamatsch - Peter Jöhr, Swisscom

Preben A. Larsen, TDC Tele Danmark

1	General Introduction	3

Definitions and Acronyms:	3

Definition of terms	3

1.1	Background	4

1.2	Purpose of the document	4

2	Technical preparations	5

2.1	Determining the origination as fixed, mobile or payphone by the IFS Access Provider	5

2.2	Separating the traffic by the originating IFS Access Provider when forwarding to the IFS Service Provider	5

2.3	IFS Service Provider recognition of the incoming IFS traffic as fixed and mobile/payphone respectively	6

3	Accounting rates, principles and guidelines	6

3.1	Determining accounting rate levels	6

3.1.1	Accounting principles for HCD in connection with mobile/payphone access (holding time vs. billed minutes)	6

3.2	Implementation (one-way or both-way)	7

4	Requirements of accounting and billing systems	7

4.1	Accounting IFS with two different accounting rates	7

4.2	Billing your IFS/HCD customers at two different rates per access country	7

5	Summary	8

# General Introduction

This document describes a proposed bilateral standard for new routing arrangements between carriers to support unique transport and settlement arrangements for  mobile and payphone originated reverse billed traffic, International Freephone Service (IFS) and Home Country Direct Service calls.

In this new arrangement, the IFS/HCD Access Provider must differentiate a mobile/payphone call from a fixed line calls and IFS Access Provider should route those calls to the IFS/HCD Service Provider differently than fixed-wire originated calls.  The proposed routing is to use more than one routing number, one for fixed, one for mobile and possibly a third for payphone originated calls.

By noticing the unique inbound mobile/payphone routing, the terminating IFS/HCD Service Provider will be able to differentiate the traffic thus providing the necessary information to settle with the originating carrier differently if required and have the ability to charge a higher collection rate to the IFS terminating customer.  The additional cost is therefore recuperated by the terminating IFS Provider, passed through the bilateral settlement process to the originating IFS Access Provider, and ultimately paid to the mobile/payphone originating carrier.

In recent years, the increase in mobile usage, combined with the decrease in settlement rates has made it impossible for the originating carriers to absorb the mobile/payphone originating costs without losing large amounts of money.  These costs vary, but tend to be in the $.18 to $.25 (US) range.  Without bilateral standards to collect these fees, many carriers have decided to stop passing the mobile/payphone originated traffic without additional compensation.

The standard described in this document allows for the transport and payment of these higher cost calls.  By adopting this standard, carriers will provide a higher level of service and ensure the future viability of their IFS services.

# Definitions and Acronyms:

# Definition of terms

IFS: International Freephone Service, including Universal International Freephone Numbering (UIFN)

IFS Access Provider: A Recognized Operating Agency (ROA) in the country of origin of the call who is responsible to ensure the establishment of access to the international freephone number in that country.

IFS provider: The Recognized Operating Agency (ROA) which provides the international freephone service to the IFS customer and is responsible for all relations with the IFS customer concerning the international freephone service.

IFS customer: The individual or entity who (or which) obtains an international freephone service from an IFS Service Provider, and is responsible for payment of all charges due to that IFS Service Provider.

IFS caller: The person who places a call to an international freephone number.

Routing number: A number format specified by the IFS Service Provider which identifies the called IFS customer and the originating country for routing purposes. The international freephone number dialed by the IFS caller is translated in the country of call origination to this special routing number before the call is transferred to the IFS Service Provider.

The above definitions are from ITU rec. E.152. Additional terms used are:

HCD Home Country Direct

UIFN Universal International Freephone Number

Product Implications used to describe implications on each solution on IFS/HCD services as seen by our customers.

Operational implications used to describe the implications on us as carriers providing IFS/HCD services.

## Background

Worldwide mobile traffic is increasing very fast. In many European countries mobile traffic is higher than fix-network traffic (I.e. Switzerland: 60% mobile 40% fix).

In European countries, mobile interconnection fees are 1000 (thousand) % higher than the one of the fix-network. Furthermore, it is anticipated that these mobile interconnection fees will not decrease more than 10% in the next 3 to 5 years. The reason is the very high UMTS (Universal Mobile Telecommunications Systems) license fees that were paid in the past. In addition the construction of the broadband mobile network will cost billions.

UMTS will play a key role in creating the future mass market for high-quality wireless multimedia communications that will approach 2 billion users worldwide by the year 2010.

From a commercial perspective, some carriers bar mobile and payphone originated calls to IFS numbers.  Here, the IFS Provider collects the revenue from the IFS customer however the IFS Provider may not compensate the IFS Access Provider for the additional cost of originating these calls.   Since there is no standard way of separately identifying mobile originated from fixed originated IFS or HCD numbers, it is difficult to transfer the mobile interconnection and payphone operator charges to the IFS Access Provider.  With the increasing trend of calling card and mobile usage, the share of mobile calls over IFS is increasing dramatically resulting in an increasingly non profitable scenario for IFS Access Providers who does not bar access.

In many countries, the regulator prescribes the use of Freecall, Freephone or Toll Free as total free of charge for the caller. As a consequence, the option for a mobile or payphone operator to recover their costs from the end user instead of the IFS Access Provider would not be possible. For prepaid or calling card markets it is crucial to be able to use payphones.   Additionally, if the IFS Provider desires to use Calling Line Identity (CLI) capability to determine if a call originates from a mobile phone and thus charge the IFS Customer and pay the IFS Access Provider, some regulators prevent passing CLI across international borders.

## Purpose of the document

This document is to further the document presented by the 2000/2001 Access Task Force regarding IFS and HCD Access from Mobiles and Payphones Issues and Recommendation

which describes various methods of separately identifying mobile originated traffic.  In anticipation of the ITU developing an international standard, perhaps in the message signal, the use of two routing numbers appears to be an alternative that is readily available between some carriers.   This document presents the how to prepare your carrier to use this capability to support continued access from mobiles and payphones to IFS and HCD services.

# Technical preparations

## Determining the origination as fixed, mobile or payphone by the IFS Access Provider

The IFS Access Provider has to be able to differentiate the origination of the different calls that go over its network. It is necessary that the IFS Access Provider receives the complete CLI’s and can determine the origination based on these CLI’s . Another option is, that the mobile switches insert an Origination Caller Identification code (OCI) and route it then to the IN platform. There the IN recognises the code an indicator of a call originating from from a mobile network.

The advantage of this method is that in countries with number portability the IN can recognise from which mobile service provider the calls come from. Also this method may make it possible to determine roaming subscribers as mobile even though the CLI is not a domestic mobile number.

Another way of determining that the caller is a roaming mobile subscriber is that the call has Forward Call Indicator = 0 (nationally originated) Nature of Address (NAI) of the CLI is set as "international". The combination of a domestic call with an International CLI only occurs for mobile roaming subscribers.

The chosen solution will, as you can see from above, depend on the national network of the IFS access country

## Separating the traffic by the originating IFS Access Provider when forwarding to the IFS Service Provider

Once the call is determined to be from a mobile network or payphone operator, the IFS Access Provider uses their switch or IN intellience to route these calls separately. based on the CLI’s, the mobile Origination Caller Identification codes or some other predetermined indicator. All calls that originate from mobile networks are routed to the the routing numbers for mobiles, all calls from the fixed network will be passed to fixed network routing numbers.

Each routing number stands for one origination and has the appropriate codes.

For example:

A) Routing number fixed network origination:

+41 801 OCI Fixnet XXXXX

B) Routing number Mobile network origination:

+41 99 802 OCI Mobile XXXXX

In this example, all calls with the numbers 801 OCI Fixnet indicate calls originating from a fixed network and 801 OCI Mobile from a mobile network. The OCI (Origination Callers Identification) indicates from which country the calls come from.

A problem could be the roamers. If the IFS Access Provider relies on CLIs as the only indicator, their switch or IN they may not recognise them as mobile origination and therefore pass the call to the wrong routing number.

## IFS Service Provider recognition of the incoming IFS traffic as fixed and mobile/payphone respectively

By virtue of the inbound routing number ranges (801 OCI Fixnet vs. 801 OCI Mobile in the previous example), the IFS Service Provider is able to recognisethe fixed vs. mobile originated traffic . All the calls that are received over routing number 801 OCI Fixnet are fixed calls all over routing number 801OCI Mobile are mobile originated calls.

There exists a risk that the IFS Access Provider sends more fixed originated traffic over the mobile phone routing number in order to collect the higher accounting rates. This has to be prevented.  One possible means to prevent this fraudulent routing is to audit the CLI of the mobile originated traffic (if it is able to be sent by the originating IFS Access Provider) to ensure the data fits with the mobile numbering range of the originating country.

# Accounting rates, principles and guidelines

In many countries there is a higher interconnection rate for Freephone traffic from mobile networks than from fixed networks and in some countries also a higher interconnection rate for calls from payphones. The purpose of the special IFS mobile/payphone accounting rate is to remunerate the IFS Access Provider for the additional costs of providing access from mobile networks and/or payphones. As the level of mobile accounting rates will vary from country to country, it is most likely that the special IFS mobile access accounting rate will be different in the two directions of a bilateral service.

It should be borne in mind that the IFS mobile access accounting is a cost covering measure and the rate should only be employed where there is a cost based reason to do so, it should not be considered an additional source of revenue/profit for the IFS Access Provider.

## Determining accounting rate levels

The basic principle behind the IFS mobile access accounting rate is that it should cover the actual costs of providing the mobile access. As mentioned above, the mobile access interconnection rate will in most cases be different in the two countries and as a consequence, the IFS mobile access accounting rate will be set at different levels in the two directions of the IFS service.

In countries where there are different interconnection rates for the different mobile operators, the IFS mobile accounting rate should be set as one amount, based on the weighted average of traffic/rates from each of the mobile operators providing access.  This average should be reviewed from time to time.

If there is no additional costs of providing access from mobile networks in a given country, or if the IDD accounting rate share is sufficiently high to cover also mobile access, there is no need to have a separate accounting rate for mobile access from that country.

### Accounting principles for HCD in connection with mobile/payphone access (holding time vs. billed minutes)

In connection with the introduction of higher accounting rates for access from mobiles/payphones, the present accounting principle for HCD accounting may need to be reconsidered. In most relations, it is common practice to only account for the number of minutes billed to the end users of the HCD service. In connection with the reduction in the IDD accounting rates, and now with the high mobile access interconnect rates, this way of accounting may no longer cover the cost of the HCD access provider.

For the access provider, the cost of providing access remains the same irrespective of whether it is an IFS or HCD call. The efficiency rate (paid minutes/holding time) of HCD service, however, will largely be dependent on the HCD service set-up offered by HCD service provider, and in the present accounting system there is no incentive for the HCD service provider to improve the efficiency rate!

One way of overcoming these problems could be to consider using network traffic (not including call set up etc. but including handling time on the card platform or operator handling time) for the basis of settlement as opposed to end-user billed traffic minutes and therefore have the same accounting rates and principles for both HCD and IFS.

## Implementation (one-way or both-way)

As the objective of developing a an accounting rate specific to IFS mobile origination is to cover additional costs in connection with access, the IFS mobile accounting rate should only be introduced where there are additional costs to the access provider.

# Requirements of accounting and billing systems

The requirements listed below are in very general terms as the implementation in each carriers systems will be dependent on the design of these systems, therefore the list mainly serves as a reminder of issues to be dealt with.

## Accounting IFS with two different accounting rates

The post-processing systems of the destination carrier must be able to determine whether the call originated from fixed or mobile.through a specific routing number series some other mechanism

In the accounting statements, there should be separate entries for IFS from fixed and for IFS from mobile and the appropriate rates should be used for each traffic type.

## Billing your IFS/HCD customers at two different rates per access country

The post processing systems for the billing of end user also needs to be adopted to be able to distinguish the origination of the call for those countries where separate prices will be used for fixed and mobile network origination.

In order for the IFS/HCD retail customer to pay the higher price for mobile, payphone access, the end user billing system will need to detail how much traffic was generated from which country and which network. There may have to be new positions introduced on the invoice statement of the retail client:

- traffic from mobile network country 1	:

- traffic from fixed network country 1  	:

- traffic from mobile network country 2	:

- traffic from fixed network country 2    	:

The content for these new positions can typically be found in the Called Party Address of the IN-Record. From the different network indicator (for example as mentioned above 801 OCI Fixnetz for fixed network or 801 OCI Mobile for mobile network) and the Origination Caller Identification code ,the country, the carrier as well as the network can be identified.

The price lists for IFS customers must be redesigned to have different rates for countries where there is a special mobile rate.

Customer order forms must be altered to provide the customer the choice of having only fixed network access or both fixed and mobile network access.

# Summary

For a midterm solution the introduction of separate routing numbers will be the only way to collect different accounting rates for mobile and fixnet access on IFS or HCD numbers. Due to this new arrangement it will be possible to keep access on IFS and HCD services open from all different networks. This will have the positive effect that IFS and HCD products will be more attractive for the customer as the availability of these services will increase. However for a long term solutions there must be an ITU standard solution.